## Slide 1
12-07-2026
1
Internship
Project
Presentation

## Slide 2
2
Presented by
  Akashay Diwan
  Adesh Jain
  Harshal Kokate
Mentored By:
  Erick Morales
APEX
LAB
APEX
LAB
Notes: Click on insert picture icon>browse picture>insert picture>go to picture properties >reduce transparency to 50%
2

## Slide 3
CAN Bus Monitoring, Simulation, and Diagnostics Platform using Raspberry Pi 5
3
APEX
LAB
APEX
LAB

## Slide 4
4
7/12/2026
Requirements
SRS · Scope
Coding & Unit Tests — the V's vertex
System Specs
Hardware & Protocol HLD
Subsystem Design
6 Modules · LLD
Implementation
Code · Algorithms
Unit Verification & UDS
UDS implementation and responses
Subsystem Integration Test
Module-level checks,encode & decode proof
System Integration Test
End-to-end bus flow
Acceptance & Use-Case Test
System validation
Following the V-Model, End to End
APEX
LAB
Notes: 8

## Slide 5
Purpose & Scope of the Platform
Built on Raspberry Pi 5 + MCP2515 (SPI CAN) + PCAN-USB(For testing), the platform establishes CAN communication, monitors and decodes live traffic, generates test frames, and validates ECU behaviour under simulated and faulted conditions.
SCOPE
  MCP2515 configuration on RPi5 over SPI
  CAN frame TX/RX — Standard (11-bit) & Extended (29-bit) IDs
  Bus monitoring, filtering & acceptance masks
  Fault generation and error-state simulation
  PCAN-USB integration for independent validation
  Diagnostic tooling and user interfaces
  Storage & visualisation of CAN traffic
1
2
3
4
5
Establish CAN communication
between embedded ECUs and host
Monitor & analyse in real time
encode & decode every frame on the bus
Generate & transmit test frames
exercise ECU responses on demand
Simulate faults & network conditions
DTCs,bus-off, errors, dropped frames
V MODEL 1/8
7/12/2026
APEX
LAB
Notes: 16

## Slide 6
Functional Requirements
the specific tasks and behaviors the system must perform to meet user needs.
SIMULATION
Generate realistic ECU CAN messages to emulate vehicle behavior for development and testing.
MONITORING
Capture, decode, and visualize live CAN/CAN FD messages with real-time signal monitoring.
DIAGNOSTICS
Perform UDS over ISO-TP communication for ECU identification, session control, and fault analysis.
LOGGING
Record CAN frames and decoded signals with timestamps in persistent storage.
6
V MODEL 1/8
7/12/2026
APEX
LAB
Notes: 11

## Slide 7
Functional Requirements
S
SIMULATION
M
MONITORING
L
LOGGING
D
DIAGNOSTICS
500 kbps standard CAN via SocketCAN, 87.5% sample point
Monitor interface state and reinitialize on error
DBC-based decoding: Physical = Raw × Scale + Offset
CAN Communication Error Handling and Retry Mechanism
Bus-off detection & automatic recovery within 5s
UDS (ISO 14229) over ISO-TP (ISO 15765-2)
RPM, Vehicle Speed & Coolant Temp ECU signal generation
Static / Ramp / Sine / Random waveform profiles
Real-time dashboard — 10 Hz refresh, <100ms UI latency
Persistent CAN traffic logging to disk
100-frame ring buffer, flushed every 500 ms
Automatic log rotation if disk is full
7
7/12/2026
APEX
LAB
Notes: 19

## Slide 8
NON
FUNCTIONAL
REQUIREMENT
the quality attributes and operational constraints of the system. They specify how the system should perform, ensuring reliability, efficiency, scalability, security, and maintainability while meeting user and business expectations.
<100ms
End-to-end latency
DEPLOYABLE ON RPI
Systems and library supporting Arm
THREADS
To run Modules Independently
MODULAR PY ARCHITECTURE
Testing for one component don’t need whole code to run
8
capture → decode → render
Easy error Identification & Scalability
Should to work on limited resoruces
Reduce lagging in system
7/12/2026
APEX
LAB
Notes: 31

## Slide 9
9
6
5
4
1
2
3
Raspberry Pi 5
Vision
Mission
Core
Values
MCP2515 (SPI)
Single CAN channel with SPI communication overhead; throughput bottlenecks may occur above ~1000 frames/sec.
PCAN-USB
USB 2.0 interface with ~1 ms polling latency; requires Linux PCAN kernel driver support.
Networking
Wi-Fi latency (10–100 ms) introduces jitter, making it difficult to satisfy the <100 ms real-time requirement.
SocketCAN/OS
Python GIL limits parallel execution; Flask development server is single-threaded, affecting responsiveness.
Power & Thermal
Wi-Fi latency (10–100 ms) introduces jitter, making it difficult to satisfy the <100 ms real-time requirement.
Quad-core Cortex-A76, 8 GB RAM, no native CAN support; relies on SPI/USB interfaces for CAN communication.
Non Functional Requirements
V MODEL 1/8
HARDWARE CONSTRAINTS
7/12/2026
APEX
LAB
Notes: 28

## Slide 10
Hardware Stack & Interface Protocols
Raspberry Pi 5
Cortex-A76 host
  CHosts the CAN monitoring application.
  Executes simulation, logging, and diagnostics.
  Interfaces with MCP2515 via SPI.
  Runs Linux with SocketCAN support.
SPI Bus
MOSI / MISO / SCLK / CE
  High-speed serial communication interface.
  Transfers commands and CAN frames.
  Full-duplex master-slave protocol.
  Connects Raspberry Pi and MCP2515.
MCP2515
CAN controller
  External SPI-based CAN controller.
  Implements CAN protocol functions.
  Handles frame transmission and reception.
  Performs arbitration, CRC, and filtering.
Transceiver
drives CAN_H / CAN_L
  Converts logic signals to differential CAN.
  Drives CAN_H and CAN_L lines.
  Provides electrical bus interface.
  Enables reliable communication on CAN.
Vehicle CAN Bus
120Ω terminated
  Shared communication network for ECUs.
  Broadcasts CAN messages in real time.
  Supports Standard and Extended CAN IDs.
  Carries vehicle sensor and diagnostic data.
10
V MODEL 2/8
Independent validation path: PCAN-USB (DB9) connects directly to the same differential bus for monitoring & cross-checks.
7/12/2026
APEX
LAB
Notes: 52

## Slide 11
Hardware Stack & Interface Protocols
SPI (Serial Peripheral Interface) enables high-speed full-duplex communication between the Raspberry Pi and the MCP2515 CAN controller, allowing efficient transmission of CAN commands and data.
  Full-duplex, MSB-first, 8-bit groups; CE LOW selects the slave
  4 SPI modes via CPOL/CPHA — MCP2515 uses Mode 0 (rising-edge sample)
  Burst read/write auto-increments internal address while CE stays LOW
CAN uses differential signalling over CAN_H and CAN_L to provide reliable, noise-immune communication between multiple Electronic Control Units (ECUs).
  Two wires, CAN_H / CAN_L — "0" is dominant, "1" is recessive
  120Ω termination at both bus ends matches characteristic impedance Z0, eliminating reflections (Γ = 0)
  Standard CAN: 11-bit ID, 0–8 bytes · Extended CAN: 29-bit ID, 0–8 bytes
  CAN FD raises payload to 64 bytes and switches to a faster data-phase bit rate (BRS) after arbitration
SPI — Raspberry Pi ↔ MCP2515
CAN Differential Signalling
11
7/12/2026
APEX
LAB
Notes: 22

## Slide 12
listener.py
SocketCAN init, non-blocking capture, struct unpacking, bus-off self-healing
SUBSYSTEM DESIGN
Six Modules, One Responsibility Each
simulator.py +encoder.py
Virtual ECU — signal generation, DBC encoding, periodic TX ,encoding to CAN frame
logger.py
Ring-buffer ingestion, 500ms bulk flush with fsync, log rotation at 100MB
uds_client.py
SID encoding, ISO-TP segmentation, P2/P2* timers, NRC evaluation
dbc_decoder.py
ID→message lookup, bit extraction, scale/offset, range validation
Dashboard.py
Flask/WebSocket live state sync at 10Hz, bus-load % computation & alerts
12
V MODEL 3/8
7/12/2026
APEX
LAB
Notes: 48

## Slide 13
Subtitle goes here
Modular Architecture
13
6/29/2026
SYSTEM-LEVEL SPECIFICATIONS
The system is designed using a modular architecture, where each component performs a dedicated function. This approach improves maintainability, simplifies testing, and enables independent development of individual modules.
APEX
LAB
Notes: 13

## Slide 14
6/29/2026
WHY LAYER IT
Each box is independently
testable and replaceable
swap MCP2515 for PCAN-USB
without touching
the CAN Service Layer
above it.
Listener — Layered Driver Architecture
14
SUBSYSTEM DESIGN · HIGH-LEVEL DESIGN
CAN SERVICE LAYER — TRANSMISSION
CAN SERVICE LAYER — RECEPTION
App Layer never sees a raw socket — only clean, validated frame objects.
V MODEL 3/8
  Determine which CAN ID should be used
  Maintain a software TX queue + retries
  TX confirmation / callback handling
  Transmission timeout monitoring
  Message routing to the right software module
  Notification & callback handling, RX queue
  Bus status reporting up to the app layer
  Application-level message timeout tracking
APEX
LAB
Notes: 13

## Slide 15
Subtitle goes here
Unified
Diagnostic
Service
13
6/29/2026
SUBSYSTEM DESIGN · HIGH-LEVEL DESIGN
Unified Diagnostic Services (UDS) is the ISO 14229 standard used for communication between a diagnostic tester and an ECU. It enables diagnostics, configuration, and software maintenance over the CAN network using ISO-TP transport.
APEX
LAB
Notes: 13

## Slide 16
DBC Decode & Encode Pipelines
Decoder — Listener to Signal
Encoder — Simulator to Bus
16
6/29/2026
THE TWO FORMULAS THAT MUST INVERT EXACTLY
Decode (raw → physical)
physical = (raw × scale) + offset
Encode (physical → raw)
raw = (physical − offset) / scale
Worked example — Vspeed
Physical = 65.0 km/h, scale = 1.0, offset = 0
→ raw = 65 = 0x41 → data[0] = 0x41
→ decode: 0x41 × 1.0 + 0 = 65.0 km/h
cantools.encode()/decode() handle the bit-level packing — start_bit, length, byte order (Intel/Motorola) — for every signal in the DBC.
V MODEL 4/8
APEX
LAB
Notes: 22

## Slide 17
Simulator — Per-Signal Generation Logic
17
SUBSYSTEM IMPLEMENTATION
· LOW-LEVEL DESIGN
INITIALIZATION
DIAGNOSTIC PROCESSING
V MODEL 4/8
  Configure CAN communication
  Initialize transport & background services
  Load vehicle state
  Start simulation loop
  Validate incoming UDS requests
  Execute requested diagnostic service
  Prepare CAN response
  Transmit result to dashboard
7/12/2026
APEX
LAB
Notes: 13

## Slide 18
End
No, unsafe
Cancel Special Session
Read a Value
Fetch Requested Sensor/Setting Value
Write a Value
Update the Requested Value
Receive and Read the Request
Background Listener running since startup
Wait for a Request from the Dashboard
Is vehicle stationary and battery healthy, if a special session is active?
Change Session Mode
Switch Diagnostic Session Normal / Extended / Programming
Unlock Access
Verify Security Key and Grant Access
Prepare Response and Queue it to Send Back
Queue for Transmission on CAN Bus
Background Sender Delivers the Response
Yes, safe / not applicable
What kind of request is it?
Control a Component
Turn a Component On/Off only allowed in unlocked sessions
Clear Fault Codes
Erase Stored Fault Codes only allowed in Programming mode
End
Read Fault Codes
Return List of Stored Fault Codes
only allowed in unlocked sessions
Firmware Update Steps
Start / Send Data / Finish Firmware Update Process
Just Acknowledge Connection
no reply needed
Are You Still There?
V MODEL 4/8
18
APEX
LAB

## Slide 19
13
6/29/2026
Dashboard
SUBSYSTEM IMPLEMENTATION
· LOW-LEVEL DESIGN
The dashboard provides a real-time visualization of vehicle data by receiving, decoding, processing, and presenting CAN messages through an interactive web interface.
Client → ECU
Diagnostic requests are transmitted over the CAN network.
ISO-TP Layer
Large messages are segmented, transmitted, and reassembled transparently.
ECU Response
The ECU executes the requested service and returns a positive or negative response.
APEX
LAB
Notes: 13

## Slide 20
Listener
20
SUBSYSTEM IMPLEMENTATION
· LOW-LEVEL DESIGN
The Listener module continuously monitors the CAN bus, receives incoming CAN and UDS frames, classifies them, and forwards them to the appropriate processing modules while coordinating transmission, logging, and timeout management.
V MODEL 4/8
7/12/2026
APEX
LAB
Notes: 13

## Slide 21
Logger
21
SUBSYSTEM IMPLEMENTATION
· LOW-LEVEL DESIGN
The Logger module records decoded CAN messages and system events using a ring buffer to minimize I/O overhead. It periodically writes buffered data to CSV files, performs automatic log rotation, and ensures reliable storage for post-analysis and debugging.
V MODEL 4/8
7/12/2026
APEX
LAB
Notes: 13

## Slide 22
UDS
22
V MODEL 4/8
SUBSYSTEM IMPLEMENTATION
· HIGH-LEVEL DESIGN
7/12/2026
APEX
LAB
Notes: 13

## Slide 23
UDS Diagnostic Session State Machine
Allowed Functions for each Session
Session | Read DID | Write DID | Upload/ Download Firmware | Download Logs | Read DTCs | Clear DTCs | IO Control
Default | ✓ | ✗ | ✗ | ✗ | ✗ | ✗ | ✗
Extended | ✓ | requires security access | ✗ | ✗ | ✓ | ✗ | ✓
Programming | ✓ | requires security access | ✓ | ✓ | ✓ | ✓ | ✓
23
V MODEL 5/8
7/12/2026
APEX
LAB
Notes: 17

## Slide 24
UDS Diagnostic Session State
UDS defines multiple diagnostic sessions that control the level of access available to the tester. Each session enables a different set of diagnostic services while ensuring secure and controlled communication with the ECU.
Extended
(0x03)
Programming
(0x02)
ECU Reset
(0x11)
Default
(0x01)
UDS
Sessions
24
7/12/2026
APEX
LAB
Notes: 34

## Slide 25
UDS Service IDs & Negative Response Codes
NEGATIVE RESPONSE CODES (NRC)
0x12 Sub-function Not Supported 0x13 Incorrect Message Length 0x22 Conditions Not Correct 0x31 Request Out of Range 0x33 Security Access Denied 0x35 Invalid Key 0x37 Required Time Delay Not Expired 0x78 Response Pending
Response Frame Shapes
Positive: [SID + 0x40] [Data] Negative: [0x7F] [SID] [NRC]
25
0x10
Diagnostic Session Control
10 03 → Extended Session
0x27
Security Access
27 01 Seed → 27 02 Key
0x22
Read Data by Identifier
22 F1 90 → VIN read
0x2E
Write Data by Identifier
2E F1 90 [data]
0x2F
I/O Control by Identifier
2F [DID][ctrl option]
0x35
Request Firmware Download from ECU
35 [DFI][ALFI]
0x19
Read DTC Information
active fault memory scan
0x14
Clear Diagnostic Information
purge DTC memory
0x3E
Tester Present
keep-alive every 2–3s
KEY SERVICE IDENTIFIERS (SID)
V MODEL 5/8
7/12/2026
APEX
LAB
Notes: 41

## Slide 26
Encoder Test
26
SubSystem Integration Test
The Encoder Test verifies the conversion of physical vehicle signals into CAN frames using DBC definitions. It ensures that signal scaling, encoding, CAN identifiers, and payload generation are accurate before transmission onto the CAN bus.
V MODEL 6/8
7/12/2026
APEX
LAB
Notes: 13

## Slide 27
DecoderTest
27
SubSystem Integration Test
The Decoder Test validates the conversion of CAN frames into meaningful vehicle signals using DBC definitions. It verifies correct extraction of signal values, scaling, and decoding accuracy by comparing the decoded output with the expected results.
V MODEL 6/8
7/12/2026
APEX
LAB
Notes: 13

## Slide 28
Simulator Test
28
SubSystem Integration Test
The Simulator Test validates the complete vehicle simulation pipeline by generating realistic driving conditions, updating vehicle states, transmitting CAN messages, and verifying real-time communication with the dashboard.
V MODEL 6/8
7/12/2026
APEX
LAB
Notes: 13

## Slide 29
Logger Test
29
Test Case | Objective | Expected Result
test_single_frame() | Verify conversion of a single CAN frame into a log record. | One log entry is generated containing the correct timestamp and CAN ID.
test_start_initializes_logger() | Verify successful initialization of the logger service. | Logger enters the running state, allocates the ring buffer, and starts the write thread.
test_push_frame() | Verify that a CAN frame is successfully added to the logger's ring buffer. | The ring buffer contains one frame with the expected CAN identifier after calling write_log().
test_stop() | Verify proper shutdown of the logger service and flushing of buffered log data. | The CSV writer is invoked to write pending logs before the logger stops.
7/12/2026
APEX
LAB
Notes: 30

## Slide 30
Nine Use Cases the Platform Must Support
ACCEPTANCE & USE-CASE VALIDATION
Monitor CAN
Decode raw frames into RPM/Speed/Temp live on dashboard
Read VIN
0x22 + DID over multi-frame ISO-TP reassembly (17-char ASCII)
Log Signal
Ring-buffer → 500ms flush → rotate at 100MB for offline analysis
Simulate ECU Nodes
Inject cyclic Ramp/Sine traffic to stand in for missing hardware
ECU Reset
UDS Service 0x11
Soft / Hard ECU reset
Restart ECU state
Security Access
UDS Service 0x27
Seed-Key authentication
Unlock protected services
Read & Clear DTCs
0x19 fault scan → P0335-style codes; 0x14 clears EEPROM memory
Change Session
UDS Service 0x10
Switch Default / Extended / Programming
Enable advanced diagnostic functions
Read ECU Information
Read ECU Identification
Software & Hardware Version
Calibration Information
30
V MODEL 8/8
7/12/2026
APEX
LAB
Notes: 15

## Slide 31
Problem Faced & Solution:
CAN Frame Reflection
  Challenge: CAN frames were being reflected on the bus, leading to unexpected communication behavior.
  Solution: Added 120 Ω termination resistors at both the ECU and tester ends to properly terminate the CAN bus and eliminate signal reflections.
Excessive Bus-Off Error Logging
  Challenge: Continuous Bus-Off errors flooded the log files, making debugging difficult and increasing log size.
  Solution: Implemented rate limiting for recurring error messages, ensuring only meaningful error events are logged.
Dashboard Latency:
  Challenge: High latency in live dashboard updates due to WebSocket communication overhead.
  Solution: Switched from WebSockets to a polling-based approach, resulting in more consistent and responsive dashboard updates.
Downloaded ZIP File Deletion Issue
Lorem ipsum dolor sit amet, consectetuer adipiscing elit, sed diam nonummy nibh euismod tincidunt ut laoreet dolore magna aliquam erat volutpat.
Encoder Masking error for extended can id in cantools library
31
7/12/2026
APEX
LAB
Notes: 24

## Slide 32
Thank You
32
7/12/2026
Notes: 67

## Slide 33
We are reimagining mobility with you
Lets collaborate
33
Notes: 68